## Slide 1: fMRI preprocessing and contrasts on SPM Julien Benistant & Valentin Guigon June 13th 2023

## Slide 2: Preprocessing on SPM

## Slide 3: fMRIPrep & BIDs format
Recent, open standard, with protocol for organizing and describing imaging data
Notes: Multiple neuroimaging tools: FSL, FreeSurfer, AFNI, SPM, etc.

## Slide 4: DICOM, NifTI & SPM
DICOM (Digital Imaging and Communications in Medicine, 1993) Current standard communication protocol used for the capture, storage and transmission of medical images and related data
NifTI (Neuroimaging Informatics Technology Initiative, NIH, 2003) A comprehensive data format used by imaging software but without a communication protocol
SPM (Matlab, 1991) One of the software specialized in analyzing NifTI images

## Slide 5
fMRI Returns a 3D array of voxels repeatedly sampled over time, with changes in activation in each voxel correlated with experimental task
Key Assumptions:
  1) The voxels need to come from the same part of the brain
  2) All voxels must be acquired simultaneously
Preprocessing: why is it needed?
Assumptions violated:
  Brain moves in the scanner
  The last slice is acquired TR seconds after the first slice
Problem: These sources of variance lower the signal-to-noise ratio
Solution: Preprocessing such as slice-timing correction (assumption 2), realignment of images (assumption 1), etc.
Notes: fMRI analysis looking at a 3D matrix of voxels repeatedly sampled over time
how fMRI works: We look at intensity of activation in a voxel at a given point of time. We plot this along with various tasks, and if activation varies with the task, we can correlate brain function.
To do this, first step we must ensure we are looking at same brain region over time.

## Slide 6: Data processing pipeline
Preprocessing
To minimize the influence of data acquisition and physiological artifacts
To check statistical assumptions and transform the data to meet assumptions
To standardize the locations of brain regions across subjects to achieve validity and sensitivity in group analysis.
Notes: Prior to analysis, fMRI data undergoes a series of preprocessing steps aimed at identifying and removing artifacts and validating model assumptions

## Slide 7: Pipeline: 1. DICOM to NifTI

## Slide 8: Pipeline: 2. Visualization
Inspect anatomical images
Look out for artifacts, such as ripples. They may be caused by subjects moving too much in the scanner
Inspect functional images
Look out for noise, transient artifacts, ghosting, dropouts, etc.

## Slide 9: Pipeline: 3. Artifact removal (optional)
Can also be done at the end of preprocessing
Beware, previous versions included a script error that needed correction by-hand
https://cibsr.stanford.edu/content/dam/sm/cibsr/documents/tools/methods/artrepair-software/ArtRepairOverview.pdf

## Slide 10: Pipeline: 4. Field Map
fMRI data is usually acquired via Echo Planar Imaging (EPI) for rapid acquisition times. The sequence acquires large amounts of gradient echoes in one TR cycle by rapidly alternating frequencies.
However, EPI is more sensitive to spatial disturbances (inhomogeneity) of the magnetic field, induced by ferromagnetic components of the magnet or the patient. The result is varying image quality + artifacts.
A fieldmap is a measure of such deviations. We use the Fieldmap toolbox to address the difference between two echoes, and to correct the distortions. The file will be used later in the preprocessing.
More at FSL Course: EPI Distortion Correction and Registration:
https://www.youtube.com/watch?v=DfGIZcEvQus
Notes: In EPI, a gradient echo is formed in the broadening direction by applying an initial dephasing gradient, and then a series of 'blips' of the opposite polarity which form the echo. The time from the r.f. excitation pulse to the centre of the echo is defined as the echo time in EPI
Gradient echoes: variations of Radio Frequency (RF) pulses : RF is switched between positive and negative

## Slide 11: fMRI parameters example

## Slide 12: Pipeline: 5. Slice timing
Correcting assumption 2:
We construct brain volumes by sampling multiple slices of the brain during each individual repetition time (TR)
Each slice is sampled at a slightly different time points
Temporal Interpolation
Use information from nearby time points to estimate the amplitude of the MR signal at the onset of each TR
• Slice time correction shifts each voxel's time series so that they all appear as sampled simultaneously.

## Slide 13: Pipeline: 6. Registration (Realign & unwarp)
Correcting assumption 1:
When analyzing the time series associated with a voxel, we assume it depicts the same region of the brain at every time point
Movements such as head motion may make this assumption incorrect
We correct that by looking for the best possible alignment between an input image and some target image (i.e., registration):
Realignment via linear transformations:
• Rigid body (6 DOF) – translation, rotation
• Similarity (7 DOF) – translation, rotation, global scaling
• Affine (12 DOF) – translation, rotation, scaling and Shearing
Unwarping:
Non-linear transformation to modify shape
We define a target image, usually defined the first or mean image in the fMRI time series
The goal is to find the set of parameters which minimizes some cost function that assesses similarity between the image and the target
To align the two images, one of them needs to be transformed via rigid body functions or non-linear functions
Notes: Shearing: shears take the diagonally opposite corners of the image and stretch them away from each other

## Slide 14: Pipeline: 7. Coregistration
We coregister the functional images to the structural image:
– Allows one to visualize single-subject task activations overlaid on the individual’s anatomical information
– Simplifies later transformation of the fMRI images to a standard coordinate system

## Slide 15
Pipeline: 8. Check registration and corrections

## Slide 16
Pipeline: 9. Segmentation (tissue probability maps)
The brain is composed of two main tissue types:
Grey matter (containing high densities of unmyelinated neurons)
White matter (containing high densities of myelinated neurons).
The brain is also surrounded by cerebrospinal fluid (CSF), and large amounts of CSF are contained in internal spaces within the brain called ventricles.
Knowing which voxels belong to which tissue type can assist in the next steps of preprocessing (Normalizing the anatomical image, warping it to match a template in standardized space).
SPM has images of six tissue priors representing their best guess as to which voxel in standardized space belongs to which tissue type. Accurately mapping the tissues of our anatomical image to the tissues of the template will increase the accuracy of our registration.
Why six? Because the anatomical image also contains non-brain tissues:
Soft tissue (e.g., dura mater)
Skull
All other tissues not captured by any of the above; usually air inside the sinuses and outside the brain, or abnormal tissue, such as tumors

## Slide 17: Pipeline: 10. Normalization
• All brains are different. The brain size of two subjects can differ in size by up to 30%
• There may also be substantial variation in the shapes of the brain
• Normalization allows one to stretch, squeeze and warp each brain so that it is the same as some standard brain
PROS
• Spatial locations are consistent
• Results can be generalized to larger population
• Results can be compared across studies.
• Results can be averaged across subjects
CONS
• Reduces spatial resolution
• Introduces potential errors
The structural MR image used in the coregistration
procedure is warped onto a template image

## Slide 18: Pipeline: 11. Smoothing
Because spatial normalization across subjects is imperfect, activations in e.g., hippocampus will not line up perfectly in a group analysis.
Spatial smoothing consists in averaging over nearby voxels (e.g., 4mm, 10mm) so it is more likely that activations overlap and therefore are detected.
CONS
The image resolution is reduced
Smoothing consists in applying a Gaussian filter to voxels:
We choose a kernel size for the Gaussian filter, called full width at half maximum (usually 3*voxel size)
The data is averaged over the width of the FWHM.
PROS
May overcome limitations in the normalization by blurring any residual anatomical differences
can cancel out the noise and enhance the signal, increasing the signal-to-noise ratio (SNR)
May increase the validity of the statistical analysis
Required for Gaussian random fields
Notes: Imagine that every subject in an fMRI experiment showed activity in a particular portion of the left inferior frontal gyrus. However, because spatial normalization across subjects is imperfect, these activations will not line up perfectly in a group analysis. Smoothing the data makes it more likely that the activations will overlap, and thus be detected, despite errors in normalization.
The standard procedure of spatial smoothing is employed by convolving the fMRI signal with a Gaussian function of a specific width.This so called Gaussian kernel is a kernel with the shape of a normal distribution curve. The size of the Gaussian kernel defines the "width" of the curve which determines in turn how much the data is smoothed. The width is not expressed in terms of the standard deviation σ, as customary in statistics, but with the Full Width at Half Maximum (FWHM). For a standard Gaussian with a mean of 0 and a standard deviation of 1, the FWHM would be 2.35: The maximum of this curve is y = 0.4 at x = 0. The half maximum is y = 0.2 at x = -1.175 and at x = 1.175. Therefore, the full width of the curve at the point of the half maximum is about 2.35. Nevertheless, the FWHM is also related to the standard deviation σ as follows: FWHM = σ √(8 ln(2)).
One common rule of thumb is that, to render your data approximately normal, you should smooth with a Gaussian filter approximately three times the size of your voxel. However, some data suggest a FHWM above 8mm is too much

## Slide 19: Contrasts on SPM

## Slide 20: Statistical analyses
Sources: Martin Lindquist and Tor Wager – Principles of fMRI (discontinued)
Notes: There are multiple goals in the statistical analysis of fMRI data.
• They include:
– localizing brain areas activated by the task;
– determining networks corresponding to brain function; and
– making predictions about psychological or disease states.

## Slide 21: GLM analysis process
Notes: Typically a two-level hierarchical analysis:
1. Within-subject (individual)
2. Across-subject (group)
• Can be done in stages (1st, 2nd level)
• Hierarchical models combine stages into one model

## Slide 22: GLM

## Slide 23: Design specification

## Slide 24: Assumptions about HRF & onsets
Single impulse onset (stimulus)
The BOLD signal follows a consistent shape, peaking around 6s then falling back to baseline over the next several seconds
Boxcar onset (stimulus)
6s
HRF overlap
Notes: Hemodynamic Response Function:
In the 1990’s, empirical studies of the BOLD signal demonstrated that, after a stimulus was presented to the subject, any part of the brain responsive to that stimulus - say, the visual cortex in response to a visual stimulus - showed an increase in BOLD signal. The BOLD signal also appeared to follow a consistent shape, peaking around six seconds and then falling back to baseline over the next several seconds. This shape can be modeled with a mathematical function called a Gamma Distribution. When the Gamma Distribution is created with parameters to best fit the BOLD response observed by the majority of empirical studies, we refer to it as the canonical Hemodynamic Response Function, or HRF.
When applied to fMRI data, the Gamma Distribution is called a basis function.
What happens if another stimulus is presented before the BOLD response for the previous stimulus has returned to baseline?
In that case, the individual HRFs are summed together. This creates a BOLD response that is a moving average of the individual HRFs, and the shape of the BOLD signal becomes more complex as more stimuli are presented close together.

## Slide 25: Nuisance covariates
Notes: May need to include:
Drift: Slow changes in voxel intensity over time (low frequency noise) is present in the fMRI signal.
  Scanner instabilities and not motion or physiological noise may be the main cause of the drift, as drift has been seen in cadavers.
  Need to include drift parameters in our models: Use splines, polynomial basis or discrete cosine basis
High-pass filtering
Physiological noise such as respiration, heart beat – that give rise to periodic noise
Motion, such as head movements

## Slide 26: Estimation (single subject GLM)

## Slide 27: Group analysis
Data is hierarchical in nature: lower-level observations nested within higher levels
1st Level
2nd Level

## Slide 28: Estimation (group GLM)

## Slide 29: Guidelines: reporting contrasts & tables
Source: Russell Poldrack – Reporting fMRI data

## Slide 30: Guidelines: reporting contrasts & tables
Better use probabilistic anatomical maps, not Talairach&Tournoux + Brodmann areas
MNI recommended (152S)

## Slide 31: Guidelines: using ROI analysis
• Characterize/explore signal
• Limit correction for multiple comparisons
• Examine functionally characterized Regions
• With complex designs, it is often difficult to tell what is going on simply by looking at maps
• Plotting signal from ROIs can be Enlightening
• Control for multiple tests over the whole brain can be highly conservative
• Limiting the number of tests (voxels) can increase power
– Only when you have a pre-existing anatomical hypothesis
– Can’t do this based on the results of another analysis of the same data!
Example
• P<.001, whole brain (2410 resells [smoothed voxels])
– Cluster with 41 voxels: • P=0.465
• P<.001, small volume correction for 10mm radius sphere (5.7 resels)
– Same cluster: p=.002
Notes: Resel = 'resolution element'.
The number of resels is a measure of volume that can be thought of as normalized for intrinsic smoothness.
It is independent of voxel size.
The size of a resel, expressed in voxels, is the FHWH of a Gaussian smoothing kernel that would produce the same smoothness in voxel-space.

## Slide 32: Guidelines: detecting outliers

## Slide 33: Guidelines: bias and circularity
Notes: E.g., If one selects only voxels in which condition A produces a greater signal change than condition B, and then evaluates whether the signal change for conditions A and B differ in those voxels using the same data, the second analysis is not independent of the selection criteria
Independence problem/Spurious correlations: Computing separate correlations for individual voxels and reporting means of only those voxels exceeding chosen thresholds
In other words, data selected on the basis of an initial statistical test are subjected to one or more further (non-independent) statistical test(s).
In statistical hypothesis testing, the most common non-independence error is referred to as ‘selection bias’. Essentially all statistical models used for hypothesis testing assume that the sampling (selection) process is independent of the relevant measure. ‘Selection bias’ is a violation of this independence assumption
The non-independence error arises in fMRI when a subset of voxels is selected for a subsequent analysis, but the null-hypothesis of the analysis is not independent of the selection criteria used to choose the voxels in the first place.
Take the simplest practical case: If one selects only voxels in which condition A produces a greater signal change than condition B, and then evaluates whether the signal change for conditions A and B differ in those voxels using the same data, the second analysis is not independent of the selection criteria

## Slide 34: Guidelines: Using neurosynth.org to obtain a priori ROIs

## Slide 35: Guidelines: transparent reporting of methods

## Slide 36: Guidelines: more publications
Poldrack, R. A., Baker, C. I., Durnez, J., Gorgolewski, K. J., Matthews, P. M., Munafò, M. R., ... & Yarkoni, T. (2017). Scanning the horizon: towards transparent and reproducible neuroimaging research. Nature reviews neuroscience, 18(2), 115-126.
Nichols, T. E., Das, S., Eickhoff, S. B., Evans, A. C., Glatard, T., Hanke, M., ... & Yeo, B. T. (2017). Best practices in data analysis and sharing in neuroimaging using MRI. Nature neuroscience, 20(3), 299-303.
Devlin, J. T., & Poldrack, R. A. (2007). In praise of tedious anatomy. Neuroimage, 37(4), 1033-1041.
Poldrack, R. A., & Mumford, J. A. (2009). Independence in ROI analysis: where is the voodoo?. Social cognitive and affective neuroscience, 4(2), 208-213.
Vul, E., Harris, C., Winkielman, P., & Pashler, H. (2009). Puzzlingly high correlations in fMRI studies of emotion, personality, and social cognition. Perspectives on psychological science, 4(3), 274-290.
Etc.

## Slide 37: Toolboxes, softwares and platforms
Toolboxes
ARTrepair: repairs scans with artifacts (e.g., head movements)
AAL1: automated anatomical parellation of T1 volumes (provided by the MNI)
AAL2: alternative parcellation of the OFC
AAL3: alternative parcellation of the anterior cingulate, thalamus and some brain nuclei
CONN: connectivity toolbox that loads .SPM designs
MarsBaR: fo regions of interest (ROIs)
Softwares
Mango: visualizer
MRIcrogl: visualizer that supports scripting; better for publications
BrainNetViewer: visualizer for connectivity; can save movies
RFXplot: data visualisation for 2nd level analyses
WFU_PickAtlas: generation of ROI masks based on the Talairach Daemon database (Brodmann area, Lobar, Hemisphere, Anatomic Label and Tissue type)
Xjview: rendering software; loads .SPM; functions for ROI selection, pValue slider, multiple images display, common area analysis, etc.
Platforms
Neurosynth.org: platform for large-scale, automated synthesis of fMRI data
OpenNeuro.org: platform for open-source validating and sharing BIDS-compliant data
andysbrainbook.readthedocs.io: comprehensive tutorials for brain data analyses, paired with https://www.andysbrainblog.com/

## Slide 38: Preprocessing on SPM – practical work

## Slide 39: Pipeline: 1. DICOM to NifTI

## Slide 40: Pipeline: 2. Visualization
Inspect anatomical images
Look out for artifacts, such as ripples. They may be caused by subjects moving too much in the scanner
Inspect functional images
Look out for noise, transient artiacts, ghosting, dropouts, etc.

## Slide 41: Pipeline: 3. Artifact removal (optional)
Can also be done at the end of preprocessing
Beware, previous versions included a script error that needed correction by-hand. Unfortunately, we forgot what was the error specifically
https://cibsr.stanford.edu/content/dam/sm/cibsr/documents/tools/methods/artrepair-software/ArtRepairOverview.pdf

## Slide 42: Pipeline: 4. Field Map
(Calculate Voxel Displacement Maps VDM), 7 steps
Same fieldmap file with the “01” suffix; located at the first fieldmap folder of each participant (gre_fieldmap_mapping…..)
2. Same fieldmap file with the “02” suffix; located at the first fieldmap folder of each participant
(gre_fieldmap_mapping…..)
3. File pm_defaults_studiesM.m
4. Choose the first image from each session of the participant
!
Keep in mind the order of sessions and use them consistently throughout the rest of the preprocessing steps.
5.
6.
7.

## Slide 43: Pipeline: 5. Slice timing
For each participant and each functional session (run 1-6), select the corresponding .nii files
These parameters were established in collaboration with Primage tech team.
TA=TR-(TR/nslices)
Type in the dialog box:
[1:2:45 2:2:45]
Specify : 1

## Slide 44
1. Use the dependency button to specify the file corresponding to each sessions (“a” suffix images ).
2. Use the dependency button to specify the file corresponding to each session
!
Mind the numbering of sessions: they are serial according to spm and not the original numbers
3. Do not modify the rest of parameters
Verify that file prefix is “u”
Phase map
Pipeline: 6. Registration (Realign & unwarp)

## Slide 45
1. Reference image: click on dependency button and select : Unwraped Mean Image
2. Specify the T1 anatomical scan (T1_MPR_SAG….Folder)
Pipeline: 7. Coregistration

## Slide 46
Select T1 anatomical image
Type: mean at the filter (right box) and select the mean image located at the folder containing the first run from the experiment.
Click Done
Pipeline: 8. Check registration and movement corrections

## Slide 47
Verify that red lines (corresponding to the functional images) follow closely the brain perimeter.
Verify anatomical features: i.e. ventricules, white and grey matter, cerebellum, etc.
Using the mouse to navigate, move around the brain volume and:
Check for mismatchs as shown below
(http://imaging.mrc-cbu.cam.ac.uk/meg/RepositioningMRIs)

## Slide 48
Using the manual alignment toolbox, adjust the images trying with different distances along the 3 axis.
Check the corrections at the Graphics window and once image is correctly fitted, click on the button
Mismatches may need to correct the alignment of the functional (EPI) image run by run.
In the file selection box,
Select all (^) “ua” prefix images
And click DONE
Launch again the check reg from the SPM menu and check that corrections were correctly applied to all runs. Use one functional image with “ua” prefix from one run and overlay on top of T1
Watch out radian units: use values < 0; i.e., 0.01

## Slide 49
T1 image
For tissue 1 to 3:
Click on Native tissue and select Native+ Dartel imported from the current box items below.
For the rest of tissues (4 to 6):
Select None
Use a batch with all participants so that all segmentation is done before doing DARTEL
Pipeline: 9. Segmentation

## Slide 50
Segmentation output are 3 images with the “RC” prefix which will be saved at the T1 folder.
rc1*.nii files = grey matter
rc2*.nii files = white matter
rc3*.nii files = CSF
Output:
rc1*.nii file
rc2*.nii file
rc3*.nii file
For each participant
Images will be saved at the T1 folder

## Slide 51
Needs all segmentation rc files and batch 1 processes to be ready before launching!
The whole procedure takes (in the order of) about a week of processing time for 400 subjects
Run DARTEL (create a template)
The Diffeomorphic Anatomical Registration Through Exponentiated Lie Algebra (DARTEL, Ashburner 2007) Toolbox is a high dimensional warping process that increases the registration between individuals, which results in improved localization and increased sensitivity in analyses.
Pipeline: 10 & 11. Normalization (DARTEL + MNI Space normalization + Smoothing)

## Slide 52
The template for all-participants will be saved at the T1 folder of the first participant:
KEEP THE SAME ORDER WHILE ADDING FILES!
The first rc1*.nii is assumed to correspond with the first rc2*.nii from the same subject, the second with the second, and so on..
Output = u_rc1*.nii file aka “flow fields”
First field will correspond to rc1 images from all subjects
Second field will correspond to rc2 images from all subjects
Third field will correspond to rc3 images from all subjects
Click at the images field and create 3 fields for each image

## Slide 53
Using dependency button, specify the last of the series of templates that was created by RunDartel (create Template). This is usually called Template_6.nii
The file is usually located at the T1 folder from first participant from the DARTEL template batch.
For fMRI analyses,
Select according to : Few Subjects
This will display new fields for adding files (see next slide)

## Slide 54
Output = smwc1*.nii files
Stored folderwise for each participant
Add as many subjects as needed and then :
Flow Field: specify the u_rc1* image of the subject (T1 folder)
Images: add all the ua functional images (type in the filter .*^ua) from all runs (training to 6)
There is no need to separate by run
Hit to run

## Slide 55: Contrasts on SPM - practical work

## Slide 56: Design specification: single-subject
Following the fMRI machine settings chosen for the experiment
TR (repetition time)
t: number of time-bins per scan
t0: reference time-bin
Select the subject’s preprocessed scans (affix: vswuaf)
Output directory
e.g., control
Vector of onset times
Vector of duration for each onset: stick function: duration=0 boxcar=real number
e.g., head movements
Vector of values

## Slide 57: Design output: single-subject
Sn(1): time series for session 1
Sn(2): time series for session 2
Inc: time series for condition with incongruent stimuli
Con: time series for condition congruent stimuli
Constant: baseline regressors that capture the mean signal for each session

## Slide 58: Estimating the model: single-subject
Select the SPM.mat for our specified design
Select Yes

## Slide 59: Contrasts specification: single-subject
t-test
incongruent (Session1&Session2) > congruent(Session1&Session2)

## Slide 60: Output: single-subject
results -> overlays -> sections -> spm12/canonical -> avg152

## Slide 61: Scripting: single-subject
The Batch module we have just created is specific to 1 subject. If you clicked on the green Go button, it would run all of the preprocessing and model estimation steps in one go. With a few adjustments, however, we can adapt this module to all of the other subjects in our study.
First, we need to save the modules into a Matlab script. Click on File -> Save Batch and Script, and label the file RunPreproc_1stLevel. Save it to the directory that contains all of your subjects. This will create a Matlab script file that you can open in the Matlab window.
From the Matlab terminal, navigate to the directory which contains the RunPreproc_1stLevel.m script, and type
open RunPreproc_1stLevel_job.m
To adapt this file so that it can analyze any subject, we will need to store in a variable the different subject numbers and place the existing code in a for-loop which will run over a set of numbers indicating each subject in the study.

## Slide 62: Design specification: group-level
Contrasts con_*.nii for all subjects
e.g., age
According to a voxel value: Explicit mask = exclusively includes voxels with that value; Implicit mask = excludes voxel with that value
Output directory
Notes: We will run a group-level analysis (also known as a second-level analysis).
In SPM, this means that we calculate the standard error and the mean for a contrast estimate, and then test whether the average estimate is statistically significant.
We will be doing this group-level analysis using a summary statistic approach which ignores the variability in the parameter estimates, and performs a t-test over the mean parameter estimates from each subject.

## Slide 63: Contrasts specification: group-level
Group-level t-test
incongruent (Session1&Session2) > congruent(Session1&Session2)
apply masking -> none
p value adjustment to control -> none
threshold {T or p value} -> 0.001
& extent threshold {voxels} -> 20
This will threshold the image to only show clusters that are composed of individual voxels each passing a threshold of 0.001.

## Slide 64: Additional notes

## Slide 65: fMRI terminology
Session. The experimental session encompasses the time that the subject enters the scanner until they leave the scanner. This will usually include multiple scanning runs with different pulse sequences, including structural, diffusion imaging, functional MRI, spectroscopy, etc.
Run. A run is a period of temporally continuous data acquisition using a single pulse sequence.
Volume. A volume (or alternatively “frame”) is single 3-dimensional image acquired as part of a run.
Condition. A condition is a set of task features that are created to engage a particular mental state.
Trial. A trial (or alternatively “event”) is a temporally isolated period during which a particular condition is presented, or a specific behavior is observed.
Event. The term “trial” and “event” are often interchangeable. However, in certain situations of ‘compound-trials,’ a trial will consist of multiple subunits; for example, a working memory task may contain subunits of encoding, delay, and retrieval. In these cases the subunits are labeled as “events” and the “trial” is defined as the overarching task.
Block. A block (or alternatively “epoch”) is a temporally contiguous period when a subject is presented with a particular condition.

## Slide 66: HRFs vary across brain regions and tasks

## Slide 67: HRFs vary across brain regions and tasks

## Slide 68: Temporal basis functions

## Slide 69: Temporal basis functions

## Slide 70: Temporal basis functions
Basis sets vary in the degree they make a priori assumptions about the shape of the response, and the HRF shapes they can account for

## Slide 71: Temporal basis functions

## Slide 72: Temporal basis functions

## Slide 73: Temporal basis functions

## Slide 74: Temporal basis functions

## Slide 75: Checking the preprocessing
https://andysbrainbook.readthedocs.io/en/latest/SPM/SPM_Short_Course/SPM_07_SettingTheOrigin.html